## Slide 1: Supporting OGC APIs: An Updated and Contemporary Approach to Geodata Provision in Disaster Mapping
Franz-Josef Behr, Lazuardy Fajar Pratama Sulaeman, Winhard
Tampubolon, Steven Fleischmann
ICCGIS 2024
Own Content is licensed under Creative Commons-License CC BY-NC-SA

## Slide 2: Outline
Introduction: Motivation & relevance
Some players (and the hurdles imposed)
Data Sources
Our implementations
  disasterGIS I: It's architecture and components
  disasterGIS II: It's architecture and data sources
Results & summary

## Slide 3: Introduction

## Slide 4: Number of deaths from disasters
https://ourworldindata.org/natural-disasters based on EM-DAT[2024-06-17] see also: https://ourworldindata.org/disaster-database-limitations
A gradual but clear upward trend […] likely to continue into the future (World Bank/ United Nations, 2010) ?

## Slide 5: Global losses from natural disasters 2013-2022
(US$ bn, inflation-adjusted, Source: MunichRe https://www.munichre.com/de/risiken/naturkatastrophen.html)

## Slide 6
„The Management […] of disasters require static geodata (for certain areas) as well dynamic geodata (i.e. flooded areas).“ (Municipal Coordination Board,Germany, 2013)
Kommunales Koordinierungsgremium (Municipal Coordination Board) GDI-DE, 2013: Einsatz von Geoinformationen in den Kommunen. Ergebnisse der Umfrage Good Practice Beispiele Handlungsempfehlungen Deutscher Städtetag; Deutscher Landkreistag; Deutscher Städte- und Gemeindebund. Berlin. Online verfügbar unter http://www.geoportal.de/SharedDocs/Downloads/DE/GDI-DE/KoKoStudie_Einsatz_Geoinfo_Kommun-nen.pdf?__blob=publicationFile.
Notes: These numbers show the importance of efficient disaster management. One fundamental element in the disaster management process is the basis of information and in particular geospatial information, as the Spatial Data Infrastructure Germany (GDI-DE) committee, an initiative of public authorities in Germany, states (Ostrau et al., 2013): „The Management […] of disasters require static geodata (for certain areas) as well dynamic geodata (i.e. flooded areas).“

## Slide 7
„The Management […] of disasters require static geodata (for certain areas) as well dynamic geodata (i.e. flooded areas).“ (Municipal Coordination Board, Germany 2013)
Kommunales Koordinierungsgremium (Municipal Coordination Board) GDI-DE, 2013: Einsatz von Geoinformationen in den Kommunen. Ergebnisse der Umfrage Good Practice Beispiele Handlungsempfehlungen Deutscher Städtetag; Deutscher Landkreistag; Deutscher Städte- und Gemeindebund. Berlin. Online verfügbar unter http://www.geoportal.de/SharedDocs/Downloads/DE/GDI-DE/KoKoStudie_Einsatz_Geoinfo_Kommun-nen.pdf?__blob=publicationFile.
Topographic data
(in vector format)
Up-to-date remotely sensed imagery (pre- and post-event)
Notes: These numbers show the importance of efficient disaster management. One fundamental element in the disaster management process is the basis of information and in particular geospatial information, as the Spatial Data Infrastructure Germany (GDI-DE) committee, an initiative of public authorities in Germany, states (Ostrau et al., 2013): „The Management […] of disasters require static geodata (for certain areas) as well dynamic geodata (i.e. flooded areas).“

## Slide 8
„The Management […] of disasters require static geodata (for certain areas) as well dynamic geodata (i.e. flooded areas).“ (Municipal Coordination Board, Germany 2013)
Topographic data
(in vector format)
Up-to-date remotely sensed imagery (pre- and post-event)
Comprise
  Terrain height, toponyms (names and unique identifiers of standard geographic areas),
  major cultural and physical infrastructure, i.e. roads, railroads, coastlines, rivers and lakes
  buildings
Are provided by
  mapping agencies (traditional approach) or
  crowd based geographical information (VGI) [Goodchild 2007]
Not available everywhere
Platforms
  Satellite-borne,
  airborne sensors (airplanes, UAVs, balloons)
Local, regional or global coverage, with certain repetition rate, swath and resolution
Automatic data processing and analysis techniques, including AI-based approaches

## Slide 9: What means „rapid“?
Rapid Mapping: “consists of the [… ] provision (within hours or days) of geospatial information in support of emergency management activities immediately following an emergency event. The products are standardized.”
International Federation of Red Cross and Red Crescent Societies (2011): IDRL Guidelines for the domestic facilitation and regulation of international disaster relief and initial recovery assistance
Emergency Mapping Guidelines drafted by the International Working Group on Satellite Emergency Mapping (IWG-SEM) 2014, https://un-spider.org/sites/default/files/IWG_SEM_EmergencyMappingGuidelines_A4_v1_March2014.pdf [2020-10-12] cited after: http://www.ithacaweb.org/projects/rapid-mapping/
Notes: Reference Maps: shows the boundaries, names and unique identifiers of standard geographic areas, as well as major cultural and physical features, such as roads, railroads, coastlines, rivers and lakes, i.e. topography
Delineation Maps: extents of the area affected by the disaster
Grading Maps: assessment of the damage grade and its spatial distribution after the disaster (in-situ or based on remote sensing data)

## Slide 10: Un-FAIR

## Slide 11: 2019:Tropical cyclones, extreme storms and floods caused overall losses of US$ 150bn
Source: https://www.munichre.com/content/dam/munichre/global/content-pieces/documents/media-relations/2019-nat-cat-world-map.pdf/_jcr_content/renditions/original./2019-nat-cat-world-map.pdf [2020-10-12]
Notes: At least in 2015 80% affected the continent of Asia, a substantially higher figure than the long-term average of approximately 70% (https://www.munichre.com/topics-online/en/climate-change-and-natural-disasters/resilience/year-in-figures.html)

## Slide 12: International Charter 'Space and Major Disasters'
a consortium of space agencies and satellite data providers, founded 1999, aiming at providing a unified system of rapid space data acquisition and delivery in case of natural or man-made disasters.
Each member agency of the Charter has committed resources to support some specified authorised users such as relief organisations as well as civil protection and defence organisations with free of charge satellite data in order to help mitigating the effects of disasters on human life and property.
The Charter data […] will be analysed by associated Value Adders, like the ZKI (with some links to CPOERNICUS).
The results are provided to the Authorized Users, requesting authorities and also to the public.
17 partners, providing data of approx. 30 satellite missions
https://disasterscharter.org/web/guest/text-of-the-charter 887 activations (until June 2024), see https://cgt.disasterscharter.org/en/887/1015
Notes: Some of the missions within the Charter are: SPOT 6/7, Pléiades, Landsat-7/8, RADARSAT 2, ALOS-2, RISAT-1, KOMPSAT-2/3 or the DMC-constellation. DLR cooperates with the Charter by providing management resources and satellite images acquired by TerraSAR-X/TanDEM-X. Additionally, DLR provides satellite images from the RapidEye mission.
The tasks of DLR ZKI are grouped into two categories:
1) The provision of the technical contribution (operations) to the Charter. This task comprises the satellite tasking and data delivery of TerraSAR-X and TanDEM-X data and the ordering and delivery of RapidEye data, the Project Management for selected Charter activations and the Emergency On-Call Officer duties. This task is supported by the Federal Ministry of Economics and Technology.
2) Value adding based on Charter data. The analysis of the data is outside the scope of the Charter. These activities are realized through other mechanisms (e.g. COPERNICUS) or organizations closely linked to the Charter. If DLR/ZKI is performing the value adding, all products are provided through the ZKI website.
Additional information about the “International Charter Space and Major Disasters” can be found on the Charter homepage.

## Slide 13: Design criteria for our rapid mapping system
All countries, institutions, agencies etc should have FAIR access to the geodata.
Software solutions should be based on open source.
Ease of installation and handling
      “Domestic actors have the primary role” [1] – the solution enables local actors to collect and provide geospatial information
    Really rapid response is needed, comprising geospatial information, to combat climate change and its impacts (SDG 13).
[1] International Federation of Red Cross and Red Crescent Societies (2011): IDRL Guidelines Guidelines for the domestic facilitation and regulation of international disaster relief and initial recovery assistance

## Slide 14: Data sources
Topographical data (vector data)
Remote Sensing Data

## Slide 15: Open Data Sources for Geographical Base Data
OpenStreetMap & Humanitarian OpenStreetMap Team (HOT)
  Geodatabase: Topographic basedata, worldwide, increasing coverage
  Mapping tools (open source)
  Processing tools (open source)
  According to Rupert Allan, former country manager of HOT Uganda, this organisation is “now the biggest contributor to the United Nations Office for the Coordination of Humanitarian Affairs […] for Uganda, and has become the go-to resource for geospatial analysis and intervention in the country“ (Politzer 2021).
Digital Elevation Models: SRTM (NASA), ASTER
Increasing amount of Open Data from national mapping agencies
…
https://wiki.openstreetmap.org/wiki/Stats [2024-06-18]

## Slide 16: Open Data Sources for Remotely Sensed Imagery
USGS EarthExplorer, https://earthexplorer.usgs.gov/
Copernicus Emergency Management Service (EMS) Mapping (started February 2015) https://emergency.copernicus.eu/
Google Earth Engine (GEE) https://earthengine.google.com/

## Slide 17: disasterGIS I
Tiers
Example

## Slide 18: Four Tier Architecture
PostgreSQL / PostGIS
File System
Map Coverage Planner
regional
extract
wget
Overpass
USGS EarthExplorer
SNAP pconvert
GDAL gdalwarp
osm2pgsql
Osmosis
Mapnik
Python
Tiles
Data Import Tier
Style File
Tiles
Data Tier
Application Tier
HTTP Server
modTile
Internet
Web Tier
Data provision
Image
Tiles
OpenStreetMap
Initial OSM Import
Remotely sensed Imagery: USGS EarthExplorer resp. Sentinels Scientific data Hub
OSM Update Sets
Notes: Vector and raster data are now available in the platform’s data tier. Mapnik (http://mapnik.org/), a well-known render tool for various OSM maps which can be seen in the application tier, is used to generate a map image resp. map tiles using the Python bindings.
https://wiki.openstreetmap.org/wiki/Mod_tile

## Slide 19: disasterGIS II
Tiers
Example

## Slide 20: Aspects
Implementation and interoperability based on based on acknowledged Web standards
  Hypertext Transfer protocol (HTTP) with its operations („verbs“) like GET, DELETE, POST etc.
    HTTP status codes
  REST-based approach (Representational State Transfer): (Re)Presentation of resources, i.e. geodata in the case of disaster as map or in a specific data format
  OpenAPI (since approx. 2016): Clear depiction of the interface of webservices („end points“) with (semi-)automatic generation of software stubs for client and server side plus documentation
  OGC‘s OpenAPI specifications (starting in 2017, now mature and ongoing)
Single Page Application: everything happens in one webpage
Looking out for promising technologies: NodeJS- allowing to use JavaScript on server- und client-side

## Slide 21: Architecture
Internet
HTTP Server
HTTP
Desktop GIS
HTML, PNG, JPG, … JSON
DBMS Server Instance
Data collection, preparation, analysis
SQL
Presentation Tier
Data Tier
Web Tier
Application Services
Server
Client
HTTP-Client
HTTP-Client
Web Browser
PostGreSQL
NodeJS
Desktop GIS
App Tier
OverPass Server
OverPass API
Internet
OSM Database
Google Earth Engine (GEE)
GEE API
Databases
GeoServer
ldProxy
HTTP
Notes: Google Earth Engine (GEE), a cloud-based platform, combines a multipetabyte catalogue of satellite imagery and geospatial datasets with planetary-scale analysis capabilities needed to detect changes, map trends, and quantify differences
on the Earth’s surface. GEE is open access and allows users to conduct analyses that would otherwise require enormous resources to access, download, store, and analyse

## Slide 22: User interface: browser-based

## Slide 23: Comparision ldproxy vs. GeoServer

## Slide 24: Administration
GeoServer: powerful, browser-based complex user interface
ldproxy: some configuration files (YAML), styling based on MapBox format

## Slide 25: Output formats
https://github.com/interactive-instruments/ldproxy/blob/master/README.md https://geoserver.org/
Ldproxy supports formats used in modern APIs, e.g. GeoJSON, Mapbox Vector Tiles, Mapbox Styles or TileJSON
GeoServer focused on traditional encodings.

## Slide 26: Performance
Ldproxy outperformed Geoserver in almost all parameters except network server latency where the latency of ldproxy is 10 and 25 times higher [Sulaeman 2024].
 | GeoServer |  | ldproxy | 
Zoom Level | 13 | 15 | 13 | 15
SI (s) | 5.8 | 7.0 | 3.5 | 2.1
TBT (s) | 3.3 | 3.2 | 2.0 | 0.1
TI (s) | 8.5 | 8.4 | 4.3 | 1.9
FID (s) | 2.6 | 2.5 | 0.4 | 0.08
NSL (s) | 0.06 | 0.06 | 0.6 | 1.5
TBW (KiB) | 5597.2 | 5597.2 | 1777.9 | 402.5
Speed Index (SI), Total Blocking Time (TBT), Time To Interactive (TI), Max Potential First Input Delay (FID), Network Server Latency (NSL), and Total Byte Weight (TBW).

## Slide 27: Summary/Limitations/Outlook

## Slide 28
DisasterGIS I – Open Source
  Completely written for Windows OS (using Windows Batch Script and Python language)
  Open Data
  Relies on the open source ecosystem (of OSGeo foundation): OSMOSIS, PostGIS, …
  Quite complex architecture, but yet easy to deploy/to install, also for „developing“ countries, small public agencies and NGOs
DisasterGIS II – Open Source, GitHub
  Operating System independent
  OpenAPI based, using ldproxy, an OGC reference implementation
  support of various data formats
  completely open source
  (almost) only open Data
  Remote Sensing Imagery: Pre- and Post-Disaster
  Interface completely browser based – user can navigate and interact in an environment he is used to

## Slide 29
Automated, rapid workflow to create a reference (online) map:
  7 minutes plus download time for vector and raster data (depending on area extent and network connectivity)
  including vector data as well as remotely sensed imagery
However:
  limited spatial resolution and accuracy (approx. 10m) for remote sensing imagery
  Limited repetion rate
  Satellite imagery can be cloud-covered
Further development should be done
  user interface,
  creation of a true map layout (for printing)
  integration of additional data sources
  creation of a user community
  dissemination of the solution.

## Slide 30: Thank you!
Prof. Dr. Franz-Josef Behr, Stuttgart University of Applied Sciences
franz-josef.behr@hft-stuttgart.de
Contact